## Slide 1: Design of an Indoor Air Quality Monitoring System using Low-Cost Sensors

## Slide 2: Contents
Introduction
Block diagram
MQTT
Node red
Sensors used
Implementation
Results
Future work
References

## Slide 3: Introduction
Indoor air quality (IAQ) as referred to by the CPCB is the quality of air inside buildings represented by concentrations of pollutants and thermal (temperature and relative humidity) conditions.
Consequences of poor indoor air quality (IAQ) have been tied to symptoms like headaches, fatigue, trouble concentrating as well as irritation of the eyes, nose, throat and lungs.
The immediate result is decline in performance of students/office employees in addition to affecting the health of the occupants.

## Slide 4: Introduction(contd…)
IAQ monitoring units available in the market are expensive.
  Smoke sensors without cloud connection cost around 5000-8000
  PM sensor cost around 9000-14000
Low cost air quality monitoring stations can be designed using inexpensive sensors to detect the presence and measure the concentration of Particulate matter(PM10, PM2.5) and high levels of harmful gases.
Although usage of low cost sensors will reduce the accuracy, air quality monitoring can be done and relative or indicative data can be published for use in smaller buildings.

## Slide 5: Block Diagram

## Slide 6: MQTT
A broker based publish-subscribe lightweight messaging protocol.
Consists of a broker(server) and clients. Both publisher and subscriber are MQTT clients.
MQTT lightweight server called eclipse mosquitto written in c has an executable file size of ~120kb, 3 Mb of ram can handle 1000 clients.
It is useful to establish connection with devices in remote locations where network bandwidth is limited or small code footprint is required.

## Slide 7: Pub/Sub in MQTT
MQTT decouples publisher from subscriber.
Publisher posts messages to a topic (address).
Subscriber subscribes to a topic to receive the messages. being published.

## Slide 8: MQTT Topics, Wildcard and QOS
Topic division is the same as file organization in a computer.
Allows Wildcard subscription
  Single level ‘+’
  Multi level ‘#’
Provides three QOS levels
  QOS 0 - at most once
  QOS 1 - at least once
  QOS 2 - only once

## Slide 9: Node-red
Is an Open source visual editor.
Developed by IBM.
Example of flow based programming model.
Provides browser based editor
Provides wide variety of easy to use ‘Nodes’.
Flows/programs are made of wired up nodes.
Flows are stored in JSON format.

## Slide 10: Nodes
Three types:
  Input nodes.
  Processing nodes.
  Output nodes.
Each node has JS file and a HTML file.
Function node for additional functionality.

## Slide 11: Dust Sensor
SDS011 dust sensor uses light scattering principle to measure PM.
Can measure PM having thickness in the range of 0.3 µm to 10 µm.
Output range – 0-999.9 µg/m3.

## Slide 12: MQ Gas Sensors
Tin dioxide(SnO2) is used as gas sensing material in MQ gas sensors.
Gases that come close to SnO2 get ionized and are adsorbed which leads to change in resistance of sensing material.

## Slide 13: Implementation Part-1
Steps performed by the sensor node and Processing unit:
Acquires readings from Gas sensors and convert it to PPM values.
Acquires data packet from Dust sensor and extract readings after verification.
Acquires readings from temperature sensor using DHT library written by adafruit industries.
Sends all the sensor readings serially to gateway.

## Slide 15: Obtaining PPM Equations
Chart: MQ-7 sensitivity characteristics
| 0.20124656299999999 | 0.14296276499999999 | 9.4208966000000421E-2 | 5.3499000000000033E-2 | 2.5423310000000148E-3 | -4.8993159000000001E-2 | -0.10191654800000002 | -0.16858420500000049 | -0.21251517400000047 | -0.25430465300000032 | -0.31442628500000208 | -0.36618266000000166 | -0.42200969000000038 | -0.46114657200000031 | -0.51705816599999799 | -0.56187653000000004 | -0.607043891000002 | -0.65047967500000226 | -0.70375867800000225 | -0.75159368300000062 | -0.79575958800000002 | -0.84216899300000003 | -0.88867827800000276 | -0.93697318600000001 | -0.98664476700000003 | -1.045387455
Carbon monoxide | 1.6972 | 1.7842 | 1.859 | 1.9293 | 2.0088 | 2.0837 | 2.1586 | 2.2335 | 2.3054 | 2.3772 | 2.4582 | 2.5331 | 2.6079 | 2.6828 | 2.7659 | 2.8394 | 2.9132 | 2.9863 | 3.0641 | 3.1383 | 3.2138 | 3.286 | 3.3636 | 3.4385 | 3.5134 | 3.6003
Hydrogen | 1.6965 | 1.7774 | 1.8523 | 1.9272 | 2.0021 | 2.077 | 2.1519 | 2.2268 | 2.3017 | 2.3766 | 2.4515 | 2.5264 | 2.6012 | 2.6761 | 2.751 | 2.8259 | 2.9008 | 2.9757 | 3.0506 | 3.1255 | 3.2004 | 3.2753 | 3.3502 | 3.4251 | 3.5027 | 3.5929
LPG | 1.7057 | 1.7802 | 1.8516 | 1.9333 | 1.9991 | 2.083 | 2.1544 | 2.2274 | 2.3038 | 2.3824 | 2.4573 | 2.5321 | 2.6043 | 2.6819 | 2.7605 | 2.8354 | 2.9132 | 2.9858 | 3.063 | 3.1378 | 3.2157 | 3.2943 | 3.3624 | 3.4407 | 3.5189 | 3.5938
Methane | 1.7029 | 1.7902 | 1.8651 | 1.9399 | 2.0148 | 2.0896 | 2.1645 | 2.2394 | 2.3142 | 2.3891 | 2.4639 | 2.5388 | 2.6136 | 2.6885 | 2.7633 | 2.8375 | 2.9174 | 2.9881 | 3.0628 | 3.1376 | 3.2125 | 3.2873 | 3.3622 | 3.4371 | 3.5179 | 3.5928
Alcohol | 1.7004 | 1.7834 | 1.859 | 1.9256 | 2.0019 | 2.076 | 2.1554 | 2.2325 | 2.3048 | 2.3822 | 2.4571 | 2.5372 | 2.6068 | 2.6816 | 2.7572 | 2.8313 | 2.9062 | 2.9811 | 3.0559 | 3.1308 | 3.2037 | 3.2805 | 3.3553 | 3.4302 | 3.5131 | 3.5889
Air | 1.6987 | 1.7856 | 1.8604 | 1.9353 | 2.0161 | 2.103 | 2.1779 | 2.2527 | 2.3247 | 2.4024 | 2.4773 | 2.5521 | 2.6247 | 2.7018 | 2.7767 | 2.8515 | 2.9264 | 3.0012 | 3.0761 | 3.1509 | 3.2258 | 3.3006 | 3.3755 | 3.4503 | 3.5252 | 3.6

## Slide 16: PPM value Calculation
Start
Print PPM
Mqpin, RL, Ratio
Calibration?
Calculate Rs
Calculate PPM
Sensor Calibration
End
No
Yes

## Slide 17: Dust sensor readings

## Slide 18
Start
Print PPM
Mqpin, RL, Ratio
Calibration?
Calculate Rs
Calculate PPM
Sensor Calibration
End
No
Yes
All gases?
Yes
No
All Sensors?
Yes
No
Dust sensor
DHT sensor
Flowchart

## Slide 20: Implementation Part-2
Steps performed by the gateway:
Establishes and maintains connection with MQTT broker.
Creates individual topics for each sensor and publishes the received readings to their respective topics.
Finally Node-red editor is used to develop a web application that subscribes and displays readings published by the sensors.

## Slide 22: Node-RED application

## Slide 23: Complete Working
Sensors send their readings to Arduino.
Arduino calculates PPM values of different gases based on Gas sensor readings, PM concentration values based on dust sensor readings.
Calculated values are serially transmitted to Raspberry pi using USB.
Raspberry pi connects to the MQTT broker and publishes the received values to various topics.
Node-red connects to the MQTT broker and subscribes to interested topics.
Node-red charts the received values using dashboard nodes.

## Slide 24: Results
Screenshot of the design file used for 3D printing
3D printed Prototype Sensor node box

## Slide 25: Results (Contd…)
Node-red flow editor: http://172.16.2.201:1880

## Slide 26: Future Scope
Cost and size of the sensor node can be further reduced.
A processing device with inbuilt wireless capability can improve the portability.
Power efficiency of the device can be further improved.
Data obtained from a large number of low cost monitoring systems placed at different points in close vicinity could be compared to arrive at a relative or indicative value.
Application can be developed to push notifications.

## Slide 27: References
Nick O’Leary and Dave Conway-Jones. (2017, January) Node-RED. [Online]. https://nodered.org/.
National AQI report. Central Pollution Control Board. [Online]. http://cpcb.nic.in/FINAL-REPORT_AQI_.pdf
Kumar, Prashant, et al. "The rise of low-cost sensing for managing air pollution in cities." Environment international 75 (2015): 199-205.
Anuj, and Gerhard P. Hancke. Kumar, "Energy efficient environment monitoring system based on the IEEE 802.15. 4 standard for low cost requirements," IEEE Sensors Journal, vol. 14, no. 8 , pp. 2557-2566, Aug 2014.
Y. C. Kan, and Y. M. Hong H. C. Lin, "The comprehensive gateway model for diverse environmental monitoring upon wireless sensor network ," IEEE Sensors J., vol. 11, no. 5, pp. 1293–1303, May 2011.